N bit adder data sheet

The circuit computes the sum of two N bits numbers, outputting a N bit number and a cary out flag that indicates an overflow.

a [N-1:0]
b [N-1:0]
res [N-1:0]
carry

N bits adder

Parameters

N – number of bits of the adder

Signals

Name	Type	Description
a	Input	Fist operand with N bits
b	Input	Second operand with N bits
res	Output	Result with N bits
carry	Output	Carry out